Lantern Data Sheet

## STRAND STAGE PROFILE
PATTERN 23 Baby Mirror Spot 500 WATT

Quantity Available  0

Price when available £35 - £50 depending on condition

Sold ex works as described, working but not Pat tested.

Can be re-wired and finished to your specification on request

Red Brick Design

Tel: 00 (44) 1872 500925  	E: enquiries@Redbrickdesign.myspacezen.co.uk

# Text boxes

Lamphouse  pressure die-cast aluminium alloy, with  top-hinged rear access.

Fork pressure die-cast, reversible, with friction disc tilt clamp and 3/8". Whit. bolt and wingnut.

Lampholder P28 medium prefocus, porcelain body, fitted with 1m external length of 3-conductor, sheathed, 	heat-resisting cable.

Reflector 180mm dia. faceted ellipsoidal rear, and annular frontal, polished anodised aluminium.

Gate Assembly (later models)four beam-shaping shutters with external heat-resisting knobs, each capable of 90° rotation around the optical axis; also gate runners.

Lens 90 x 125mm piano-convex in sliding lens tube.

Colour Frame double die-cast runners fitted.

Lamps 500W max. P.28 base. 55.5mm Class T/1 recommended for stage use.

Beam Spread Cut-off 20° max. 1/2 deg peak angle 20° 3m spread at 8.5m throw